## Slide 1: ML605 MultiBoot Design
May 2010
© Copyright 2010 Xilinx
XTP043

## Slide 2: Overview
MultiBoot Capability
Xilinx ML605 Board
Software Requirements
Compile ML605 P30T BPI MultiBoot Design
Program ML605 with P30T BPI MultiBoot Design
Run MultiBoot Design
References
Note: This presentation applies to the ML605

## Slide 3: Virtex-6 MultiBoot Capability
Multiple Bitstreams for Multiple Missions
  E.g. Power-On self test followed by final application
  Hardware assisted system testing
MultiBoot Capability
  FPGA Application controlled configuration
  Bitstream selection
Safe Update
  Golden bitstream
  Upgradeable bitstream
  Failure recovery
    Possible Triggers (CRC error, IDCODE error, WDT timeout)
Note: Presentation applies to the ML605

## Slide 4: Virtex-6 MultiBoot State Machine Flow Diagram
ICAP Based Designs for Virtex-6 MultiBoot

## Slide 5: Virtex-6 MultiBoot State Machine Flow Diagram

## Slide 6: Xilinx ML605 Board
Note: Presentation applies to the ML605

## Slide 7: ISE Software Requirements
Xilinx ISE 12.1 software
Note: Presentation applies to the ML605

## Slide 8: Compile ML605 P30T BPI MultiBoot Design
Unzip the rdf0007.zip file to your C:\ drive
  Available through http://www.xilinx.com/ml605
Note: Presentation applies to the ML605

## Slide 9: Compile ML605 P30T BPI MultiBoot Design
Compile the BPI Flash:
    cd C:\ml605_multiboot
    run_script.bat
Note: This step takes about seven minutes

## Slide 10: Program ML605 with P30T BPI MultiBoot Design
Power on the ML605 board
Connect a USB Type-A to Mini-B cable to the USB JTAG connector on the ML605 board
  Connect this cable to your PC
Note: Presentation applies to the ML605

## Slide 11: Hardware Setup
Set S2 to 001010 (1 = on, Position 6  Position 1)
  This selects P30T BPI
  Mode Switches set to BPI-Up
Set S1 to 0XXX (X = Don’t care, Position 4  Position 1)
  This disables JTAG configuration from the Compact Flash
Note: Presentation applies to the ML605

## Slide 12: Program ML605 with P30T BPI MultiBoot Design
Run iMPACT
    impact
Note: Presentation applies to the ML605

## Slide 13: Program ML605 with P30T BPI MultiBoot Design
Select:
  Create a new project
  Configure devices using Boundary Scan (JTAG)
Note: Presentation applies to the ML605

## Slide 14: Program ML605 with P30T BPI MultiBoot Design
Right-click on SPI/BPI and select Add SPI/BPI Flash…
  Select the <Design path>\iMPACT\bpi_p30_Rev01.mcs
Note: Presentation applies to the ML605

## Slide 15: Program SPI MultiBoot Design
In the Select Attached SPI/BPI GUI, select
  BPI PROM
  28F256P30
  Data Width: 16
  Address Bits: 24:23
Note: Presentation applies to the ML605

## Slide 16: Program ML605 with P30T BPI MultiBoot Design
Program the BPI Flash:
  Right-click on the Flash and select Program
Note: Programming takes about 45 minutes with verification

## Slide 17: Program SPI MultiBoot Design
Erase Before Programming must be selected
Cycle Board power when programming is complete
Note: Presentation applies to the ML605

## Slide 18: Run MultiBoot Design
The initial LED flashing pattern, Module A will appear
Press SW9 (center button) to go to the next pattern
  The DONE led (DS13) will go out momentarily
  The ML605 will load the new bitstream from flash and display the next pattern

## Slide 19: Run MultiBoot Design
The second LED flashing pattern, Module B will appear
Pressing SW9 again will return to the initial pattern

## Slide 20: References

## Slide 21: References
Virtex-6 Configuration
  Virtex-6 FPGA Configuration User Guide
    http://www.xilinx.com/support/documentation/user_guides/ug360.pdf

## Slide 22: Documentation

## Slide 23: Documentation
Virtex-6
  Virtex-6 FPGA Family
    http://www.xilinx.com/products/virtex6/index.htm
ML605 Documentation
  Virtex-6 FPGA ML605 Evaluation Kit
    http://www.xilinx.com/products/devkits/EK-V6-ML605-G.htm
  ML605 Hardware User Guide
    http://www.xilinx.com/support/documentation/boards_and_kits/ug534.pdf
  ML605 Reference Design User Guide
    http://www.xilinx.com/support/documentation/boards_and_kits/ug535.pdf